## Slide 1: 12/18

## Slide 2: Optical truss sideband locking
Closed the loop
  Moku LLB error fed back to VCO, to drive EOM and sideband lock
Brief (~1 minute) sideband lockings achieved using Moku LLB and laser piezo actuation, with laser freq. adjustment
  Quickly drifts out of sideband resonance, will require optimization

## Slide 3: Simulations (RX/Long-arm TTL)
Expanding simulation parameter space
  More agreement check of Alex/Paul formulations
  Verification of regular vs. total LPS performance for long-arm IFO
Contrast comparisons
  Investigate total LPS limitations
  Not trivial calculation in Paul’s current formulation
Material for annual write-up
  Plots showing agreement Alex/Paul/Paul F(numerical TH-HG00 check)
  Probably not timing or expansion order variation (Paul)
  Plots for shot noise, contrast (Alex)